## Slide 1: CIRRUS SR20/SR22
Circuit Electrique

## Slide 2: CIRRUS SR20/SR22

## Slide 3: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
GENERALITES
  28 Volt DC
  Negative Ground
  Dual Alternator
  Dual Battery
  The system provides uninterrupted power for:
    the avionics,
    flight instrumentation,
    lighting,
    and other electrically operated and controlled systems during normal operation.

## Slide 4: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
SCHEMATIC

## Slide 5: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
COMPONENTS
  Alternator 1
    100/60 Amp (60 amp no A/C)
    28 Volts
    Gear driven
    Internally rectified
    Self exciting (requires battery voltage for field excitation in order to start operating)
    Powers Main Distribution bus directly and Essential Bus indirectly

## Slide 6: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
COMPONENTS
  Alternator 2
    20 Amp
    28.75 Volts
    Gear Driven
    RPM dependant < 1700 rpm it will not work
    Internally rectified
    Self exciting (requires battery voltage for field excitation in order start operating)
    Powers Essential Bus
    Cannot power Main Distribution Bus (diodes)

## Slide 7: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
COMPONENTS
  Battery 1
    Aviation grade 12-cell
    24-Volt
    10 amp-hour
    Mounted on right side of firewall
    Charged by Alt 1 through Main Dist Bus
    Can supply power to the Main and Essential Distribution Buses

## Slide 8: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
COMPONENTS
  Battery 2
    Two 12 volt batteries in series = 24 volts total
    7 amp-hour
    Sealed lead acid
    Located in the tail of the airplane below the parachute canister
    Charged by Alt 1 or Alt 2 from a circuit breaker on the Essential
    Distribution Bus
    Powers Essential DistributionBus only due to isolation diodes

## Slide 9: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
COMPONENTS
  Master Control Unit (MCU)
    Controls: ALT 1, ALT 2, starter, landing light, external power and generation functions
    Provides:
      ALT 1 and ALT 2 voltage regulation and overvoltage protection
      External power reverse polarity protection
      Electrical health annunciations to the Integrated Avionics System

## Slide 10: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
COMPONENTS
  ISOLATION DIODES
    Electrical “check valves” or “one way street”
    Electricity can only flow in the direction of the arrows
    Prevent ALT 2 from powering the Main Distribution Bus
    Prevent BAT 2 from powering the Main Distribution Bus
    Check operation of diodes during preflight by turning only BAT 2 on
    and then verifying flap position light is out

## Slide 11: CIRRUS SR20/SR22 ELECTRICAL SYSTEM

## Slide 12: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
ELECTRICAL SYSTEM CONTROLS
  MASTER SWITCHES
    Rocker type electrical system master switches are located in front
    of the pilot on the bolster panel for easy access.
  CIRCUIT BREAKER PANEL
                Located on left side of center console
                Alternating gray collars on the CB panel provides easier recognition
    of circuit breakers
                Circuit breakers are re-settable (once) !

## Slide 13: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
ELECTRICAL SYSTEM CONTROLS
  CIRCUIT BREAKER PANEL

## Slide 14: CIRRUS SR20/SR22 ELECTRICAL SYSTEM

## Slide 15: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
NORMAL OPERATION
  ALT 1_ 28 volts
    Supplies power to Main Dist Bus
    Charges BAT 1
    Powers Essential Bus when aircraft is < 1700 rpm

## Slide 16: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
NORMAL OPERATION
  ALT 2_ 28,75 volts
  Supplies power to the Ess Bus during cruise flight
  (>1700 rpm) because it operates at a higher voltage
  Water analogy- Think of higher voltage as higher
  pressure (water) running through the wires (pipes).
  The higher voltage (pressure) of ALT 2 prevents ALT 1
  from powering the Ess Bus
  Charges BAT 2
  Diodes prevent ALT 2 from powering the Main Dist Bus
  Click on diagram to see “normal” engine indications

## Slide 17: CIRRUS SR20/SR22 ELECTRICAL SYSTEM

## Slide 18: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
ABNORMAL OPERATION
  INDICATION OF AN ALT 1 FAILURE
    Steady “ALT 1” caution light on annunciator panel
    Main Bus (M.BUS) indicates a decreased voltage
    Battery 1 (BATT) indicates a discharge
    Verify on MFD engine page or ampere meter switch
      ALT 1 (A)- 0
      ALT 2 (A) – Normal
      BATT 1 (A) discharging -12
        How long will it last?
        How to reduce drain on BATT 1?
      Ess (V)- 28.7 ALT 2
      Main (V)- 24.2 Bat1
ALT 1

## Slide 19: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
ABNORMAL OPERATION
  ABNORMAL PROCEDURE ALT 1 LIGHT STEADY
    Analysis
    Procedure
      ALT 1 Master Switch – OFF
      Alternator 1 Circuit Breaker – CHECK and RESET
      ALT 1 Master Switch – ON
      Switch off unnecessary equipment on Main Bus 1, Main Bus 2, and the
      Non – Essential Buses to reduce loads. Monitor voltage
      ALT 1 Master Switch – OFF
      Land as soon as practical (continue flight, avoiding IMC or night conditions)
ALT 1

## Slide 20: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
ABNORMAL OPERATION
  DISCUSSION ALT 1 FAILURE
    BAT 1 powers Main Bus items
      Turn off these items to reduce discharge
      of BATT 1 if ALT 1 fails
      Some items on the main bus have a primary
      circuit breaker on the Ess bus (#1). These
      items will be powered by ALT2 through
      the Ess Bus (higher voltage)
        Turn coordinator (hidden behind right
        bolster panel to provide roll information
        to the autopilot)
        Attitude indicator
        HSI/PFD
    ALT 2 continues to power Ess Bus items
    Complete ALT 1 failure checklist to attempt reset of ALT 1

## Slide 21: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
ABNORMAL OPERATION
  ALT 2 FAILURE
    Steady “ALT 2” annunciator panel
    Verify on MFD engine page or ampere meter switch
      ALT 1 (A)- 12 Normal
      ALT 2 (A) – 0
      BATT 1 (A) Normal
      Ess (V)- 28- Alt1
      Main (V)-28- Alt1
ALT 1
ALT 2

## Slide 22: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
ABNORMAL OPERATION
  ALT 2 FAILURE
    < 1700 RPMS ALT 2 will not work
    ALT 1 will power the entire electrical system
    Follow ALT 2 failure checklist and try to reset ALT 2
    ALT 2 is required for IFR flight

## Slide 23: CIRRUS SR20/SR22 ELECTRICAL SYSTEM

## Slide 24: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
GROUND OPERATION
  GROUND SERVICE RECEPTACLE
    Allows connection of an External Power Unit for
    cold weather starting and maintenance
    BAT 1 switch must be on to deliver power to system
    BAT 1 must have power for the contactor to close
      Recharging of BAT 1 should not be accomplished
      through use of an External Power Unit
      External Power Unit voltage must be regulated
      to no higher than 28 VDC

## Slide 25: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
QUESTIONS
  PREFLIGHT CHECK LIST
    During the preflight check, why do we initially turn BAT 2 on only ?
      Allows the pilot to check voltage (health) of BAT 2
      To verify the isolation diodes are operating correctly- flap light out

## Slide 26: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
QUESTIONS
  PREFLIGHT CHECK LIST SCENARIO
    During the preflight check with only BAT 2 on, you noticed the flap light was on.
      Would you still depart for your flight?
      Why or why not?
      Go or No Go ?
      The isolation diodes are not working correctly.
      ALT 2 would then try to power the entire electrical
      system. ALT 2 is 20 amps and not powerful enough
      to power Main Distribution Bus items. This most
      likely, will cause ALT 2 to fail.
      The pilot would be unable to isolate items on the
      Essential Distribution Bus in an emergency.
      BAT 2 would try to the power Main Distribution Bus.

## Slide 27: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
QUESTIONS
  FLIGHT SCENARIO
    Looking at your engine data in cruise, this is what you see.
      Has anything failed?
      What are you going to do?
ALT 1 has failed. Perform ALT 1 failure checklist.

## Slide 28: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
QUESTIONS
  FLIGHT SCENARIO
    Looking at your engine data in cruise, this is what you see.
    Has anything failed ?
    What are you going to do ?
ALT 2 has failed. Perform ALT 2 failure checklist.

## Slide 29: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
QUESTIONS
  FLIGHT SCENARIO
    You are 30 minutes out from your destination
    and you begin to smell something. After
    investigating you see white smoke rising
    from the circuit breaker panel.
      What is happening ?
      What will you do ?
      Will your procedure be different in VMC vs. IMC ?
      Day vs. Night ?

## Slide 30: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
QUESTIONS
  FLIGHT SCENARIO
    You are 30 minutes out from your destination
    and you begin to smell something. After
    investigating you see white smoke rising
    from the circuit breaker panel.
      What is happening ?
      What will you do ?
      Will your procedure be different in VMC vs. IMC ?
      Day vs. Night ?

## Slide 31: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
RESOURCES
  SIMPLIFIED ELECTRICAL DIAGRAM

## Slide 32: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
RESOURCES
  SIMPLIFIED ELECTRICAL DIAGRAM

## Slide 33: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
RESOURCES
  FAILURE MESSAGES

## Slide 34: CIRRUS SR20/SR22 ELECTRICAL SYSTEM
QUESTIONS ?